User Command :
              DRAWGRID - Draw Full Grid for drawing

              GRIDA    - Draw Internal Grid for drawing
                         with CROSS1.DWG

              GRIDB    - Draw Out Bound Grid for drawing,
                         with CROSS1.DWG

              N        - Pick point on drawing
                         and plot a table of points coordinates
                         with point's number or name.

              PLOT3D   - Manually add points on Drawing.
                                                    
              PTID     - Pick Point and plot Coordinate on drawing.
                         
              SLOPE    - Draw a slope symbol at pointing location.

              LN       - Draw different line type, with LN#.DWG

             BLK       - Draw different Blocks type, with LN#.DWG
                         
              KTSC     - Draw Spiral Curve, with tsc.dcl file

              DIK      - Change Height of Text, radius of Circles
              
              S2TY     - Make Section file in Text format for PCSUR. 

              IDFL     - Select points on drawing and save them
                         into Text file of NEH format for PCSUR.

Note :

         Sometimes as you run DRAWGRID then the scale factor has been set,
         so that the text size may be not you wanted,then change the
         scale by type in (setq g:scale ####) at ACAD command prompt.
         #### is the scale that you want.

         Make sure the CROSS1.DWG file is located in \acad\support directory
         before running GRIDA and GRIDB.
         
         Running GRIDB you may found the text rotated direction is not normal. 
         First, check the direction for your drawing in pull-down menu
         ( setting -> unit control -> direction ) set it back to the original
         setting ( 0 degree is to the right and in counterclockwise direction
         ). Second, type "text" in the command prompt check the current  
         rotation angle for the "text" command to see whether it is set to the
         default setting ( 0 degree ) if not set it back.

         Running LN , make sure the LN#.DWG file is located in \acad\support
         directory, and check the direction for your drawing in pull-down menu
         ( setting -> unit control -> direction ) set it to the drection 
         0 degree to the top ( North ).
         You can change any line type you want, as you can change the LN.DWG 
         file and save it as LN#.dwg as you like.

         Running KTSC program, make sure the TSC.DCL file is located in the
         \acad\support directory.
         The start point for drawing a spiral curve ( in or out )  
         is always the point that tangent to the straight and end point is 
         always the point that tangent to the simple curve.

         Running S2TY , it can only select "line" entities for data 
         processing so that joint lines between spot level points crossing 
         the section line and to ensure no data missing change all lines to
         CONTINUOUS before running the S2TY program. 
         The first section will cut at the start point of the reference line
         and it's default chainage is 10.
         The output file located in the current directory or in the path that
         you specified with the extension TXT.